## Slide 1
PAPER-A · GROUP MEETING SYNC
Feel It, See It, Recover
Cross-Modal Failure Attribution for Safe
Quadrupedal Navigation Recovery
Object of study: resolving conflicts between body sensing and vision to choose the right recovery — not a full navigation-system paper.
Evidence stack: A0–A7 complete on real Unitree Go2 + Isaac / RTX · A8 optional hardware snapshots
Claims C1–C5 · Designs A0–A7 · Results · Claim bridges

## Slide 2
1. Problem & evaluation currency
Why attribution — not closed-loop reach — is the object of study
THE FAILURE MODE
A quadruped can “see” safe terrain while its body feels a different physics — or the reverse.
Proprioception = body sensing (joint torques, contact, effort).
Vision = RGB / appearance of the scene.
Attribution = naming the physical cause so the right recovery is selected.
EVALUATION CURRENCY
Frozen failure snapshots — record one decision window at anomaly onset; re-score many agents on the same disk set.
Interventional consequence — swap only the attributed label and measure physical cost (fall, strand, detour), not “agent race” navigation scores.
WHAT THIS PAPER IS / IS NOT
Is: cross-modal conflict resolution as a learned semantic operation + causal link to recovery safety.
Is not: a SLAM / map / CBF-shield / locomotion-policy paper. The full KiNO stack (monitor, VLA planner, shield) is infrastructure.
VLA = Vision–Language–Action model (here: Qwen3-VL-4B with LoRA + Kino-Tokens). Kino-Tokens = learned latent body summary injected into the VLA.
Paper-A progress sync · real-stack evidence only · A8 optional
2 / 12

## Slide 3
2. Claims C1–C5 (plain English)
Each claim has independent experimental legs (see later slides)
C1
Necessity, both directions
Some failures are invisible to body-only models (matched sticky vs soft terrain). Others need body sensing because vision is wrong or blind. Neither modality is enough alone.
C2
Learned conflict resolution
Having a vision channel ≠ using it for evidence weighing. Conflict competence must be trained; bidirectional conflict is the stress test.
C3
Attribution ⇒ recovery / safety
Wrong cause labels change physical outcomes under a fixed scene (label-swap). Costs are asymmetric → principled safe defaults under uncertainty.
C4
Generalization + abstention + boundary
Works on held-out looks/compositions; abstain when uncertain; locate when to intervene vs continue (θ* on effort decay; O2 is modality-dependent).
C5
Fair opponent
The pure-body baseline B1 is strong on ordinary cases (~0.76 fidelity), so its failure on matched conflicts is by construction — not under-training.
Paper-A progress sync · real-stack evidence only · A8 optional
3 / 12

## Slide 4
3. A0 — Shared evaluation infrastructure
Why every later number is trustworthy
A0.1 Determinism
Why
Same scenario in different run orders must agree.
Result
deep_reset + fixed geometry: max|Δ|=0; same-op C2ST ≈ 0.5. Controls fail when residual left in place.
Bridge
Gates all closed-loop numbers (A4/A6).
A0.2 Triggers
Why
Attribution is scored given an event.
Result
Oracle-primary (privileged onset). Optional realistic monitor for robustness only.
Bridge
Isolates attribution from detector tuning.
A0.3–A0.5 Corpus
Why
All agents see the same frozen set.
Result
≥100 snapshots / taxonomy cell; appearance train/test split; success & admissible-recovery registry.
Bridge
Enables McNemar paired tests; blocks color shortcuts.
Paper-A progress sync · real-stack evidence only · A8 optional
4 / 12

## Slide 5
4. C1 — Necessity (both directions) · Experiment A1
Matched pairs + mirror taxonomy cells
Design motive: Prove neither pure vision nor pure proprioception subsumes the other — with certified indistinguishability, not intuition.
O4 sticky ↔ O2 soft terrain
Matched pair: same force-law family; body stream made to match.
Proprio byte-identical: max|Δobs48+τ| = 0.0
C2ST (classifier two-sample test) ≈ 0.5 on body features (cannot tell them apart).
Vision (CLIP) separates perfectly (AUC = 1.0).
T3 mirror: O7 / O8
Vision misleading or blind; body is decisive.
1-D CNN proprio attribution ≈ 1.0 on the decisive side.
CLIP vision near chance / blind on same-appearance pairs (~0.31).
O3↔O1 demoted after certification failed to close — taxonomy stands on O4↔O2 + T3.
Claim bridge: If either modality alone sufficed, one of these constructions would collapse. Falsifier = proprio C2ST ≫ 0.5 on matched O4↔O2, or vision solving T3 mirror alone.
Paper-A progress sync · real-stack evidence only · A8 optional
5 / 12

## Slide 6
5. C2 — Learned conflict resolution · A2 + A3 (+ C5)
Three-row scale-up and bidirectional evidence weighing
Why: n=240 matched conflict snapshots; appearance held-out; open-loop single decisions. Separates “has vision” from “uses vision for conflict.”
B1 pure proprio
0.50
Strong body-only baseline (C5 fair opponent; unshaped fidelity ≈0.76)
B5-unshaped / vision-capable
0.80
Has vision + body; no conflict curriculum
B5-conflict
0.90
Same model + matched conflict samples
McNemar B1 vs B5-conflict: b=0, c=24, p<1e-5 · 3 seeds all 0.90 · held-out appearance split survives
A3 bidirectional battery (T3)
B-V fails T3 (O7≈0.19 / O8≈0.00). B1 complements on O8 (100%). B5-conflict-bi solves T3 ≈ 0.92 and is proprio-driven across 3/3 seeds — not “always trust camera.”
C2 bridge: Conflict competence is trained, not free with a vision channel. Falsifier = B5-unshaped matches B5-conflict, or B5-conflict-bi is vision-dominant on reverse probes.
C5 bridge: B1 is a strong ordinary-case attributor (≈0.76 fidelity), so its matched-conflict failure is by construction — not under-training. Falsifier = weak B1 on unshaped ops.
Paper-A progress sync · real-stack evidence only · A8 optional
6 / 12

## Slide 7
6. C3 — Attribution causes recovery / safety · A4
Label-swap matrix: same scene, different attributed cause
Why: Closed-loop “agent races” confound many things. A4 freezes the world, oracle-triggers once, and scripts recoveries — only the label ℓ changes. 630 episodes (9 scenarios × 7 labels × N=10).
1.00
Canonical success
[0.72, 1.00] Wilson
0.00
Off-diagonal crux
[0.00, 0.28]
4×
T2 cost
antisymmetry
0.11 vs 0.44
Conflict-agent regret
vs baselines
Safe default: under uncertainty, prefer the action whose wrong-label cost is lower. Crossover p*(adhesion) ≈ 0.25.
ERS / Regret: expected recovery cost / excess cost vs best label — map attributions into physical cost units without a new agent race.
Claim bridge: If attribution were decorative, the label-swap matrix would be flat. Falsifier = diagonal ≈ off-diagonal on crux cells.
Paper-A progress sync · real-stack evidence only · A8 optional
7 / 12

## Slide 8
7. C4 — Generalization, abstention, boundary · A5 + A6
Held-out looks; when to say “I don’t know”; when to intervene
A5 — Generalization & abstention
Why: Kill color shortcuts and show calibrated “hold”.
Appearance OOD: B-V −0.21 worst; B1 −0.03 least.
OOD-θ residual: distance of privileged θ from training support — abstain when large.
LOO-O5: residual 16.09 → Hold → 100% safe.
Abstention AUROC 0.87; risk–coverage best expected cost 1.63 < always-intervene 2.80 and never-intervene 1.71.
Composition: 16/16 held-out operator mixes.
A6 — Intervention boundary
Why: θ* must be agent-independent (privileged base).
O10 effort decay θ* = 0.2754 — base reach 1.0 above floor 0.3; 0.0 below 0.25.
OOD-θ residual tracks θ* (0.629 → 0.949; crosses ~0.85).
O2 modality dependence: proprio may fire while cross-modal agent attributes mild compliant terrain.
Honest: literal continue/intervene flip weaker; residual-tracks-θ* is the reportable result.
C4 bridge: Attribution must travel OOD and know when to abstain or intervene. Falsifier = appearance OOD kills all agents equally, residual uncorrelated with θ*, or risk–coverage never beats always/never intervene.
Paper-A progress sync · real-stack evidence only · A8 optional
8 / 12

## Slide 9
8. C2 methods — A7 ablations (protocol-clean)
What ingredients actually carry conflict competence
Latent vs text
(M7 route)
Controlled injection: same VLM, change only body encoding.
Vision-only amb. 0.458 vs text/latent 1.0; latent adds θ head; 1.27× fewer tokens than binned text.
Conflict dose
Unique-sample doses {0,5,10,20,40} × 3 seeds; same SFT recipe.
Best mean O4 attr at dose 10 = 0.733; best A4 regret 0.40. Dose 5 unstable under protocol (mean 0.333) — reported honestly.
Truth filter
+ grounding
ApiOracle CoT kept vs dropped; same checker on emitted thoughts.
Grounded-correct 0.604 → 0.765 after filter; test-time emitted GC up to 0.8.
Encoder grid
+ A7.1
Privileged / contrastive / scratch × T × gate; posterior abstention.
18/18 cells; θ MAE 0.0279 privileged. Entropy held-out cost 1.469 < safe-default 1.633.
Paper-A progress sync · real-stack evidence only · A8 optional
9 / 12

## Slide 10
9. Claim × experiment map
Core ● support ○ — every claim has ≥1 strong leg
A1
A2
A3
A4
A5
A6
A7
C1 necessity
●
○
●
·
·
○
·
C2 conflict learn.
·
●
●
·
·
·
●
C3 consequence
○
·
·
●
○
·
·
C4 gen./boundary
·
·
·
·
●
●
○
C5 fair opponent
●
●
·
·
·
·
·
Reading guide: A0 is infrastructure for all. A8 (real-world snapshots) is optional and not load-bearing. Method ablations (A7) support C2 without reopening C1/C5.
Paper-A progress sync · real-stack evidence only · A8 optional
10 / 12

## Slide 11
10. Status, honest scope, next steps
What is done — and what we will not oversell
DONE (REAL STACK)
A0–A7 complete on Isaac physical Go2 + RTX.
All headline metrics from frozen snapshots / label-swap / privileged sweeps — no CPU surrogate, no ScriptedOracle as primary stream.
Manuscript: problem-first ICRA draft exists (paper/main.tex).
Fast gate: pytest -m "not slow" green.
HONEST LIMITS (NOT HIDDEN)
A7 dose knee is protocol-matched dose 10; unequal-recipe dose-5 “fixes” are sensitivity only.
Greedy latent vs text ties — latent wins on θ + tokens, not forced accuracy gap.
A6: residual tracks θ*; literal snapshot flip weaker.
Sim physics (spring-damper adhesion, etc.) is approximate.
A8 hardware snapshots optional if time free.
Pending human sign-off: deep_reset as standard collection; #49/#52 wording in paper.
Paper-A progress sync · real-stack evidence only · A8 optional
11 / 12

## Slide 12
11. Glossary (quick English glosses)
Specialist terms used in this deck
Proprioception
Body sensing: joint angles/torques, contact, effort — not cameras.
VLA
Vision–Language–Action model that outputs recovery actions from image + body.
Kino-Tokens
Learned compact latent summary of the body window fed into the VLA.
C2ST
Classifier two-sample test: can a model tell two distributions apart? ~0.5 = no.
Matched O4↔O2
Sticky adhesion vs soft compliant terrain built so body streams match.
θ / OOD-θ residual
Privileged physics parameter; residual = how far from training support.
θ*
Severity where base policy stops succeeding without intervention (agent-independent).
Label-swap matrix
Fix the scene; change only the attributed cause; measure outcomes.
McNemar / Wilson CI
Paired accuracy test / binomial confidence interval on rates.
ERS / Regret
Expected recovery cost / excess cost vs best possible label.
B1 / B5-conflict-bi
Strong pure-proprio baseline / VLA trained on both conflict directions.
Abstention
Refuse to act / hold when uncertainty is high; pay safe-default cost.
Paper-A progress sync · real-stack evidence only · A8 optional
12 / 12